## Slide 1
Lab 1: Verifying a Timer Using UVM RAL Objective
Integrate a generated UVM register model into a working UVM environment and prepare it for RAL-based testing.
SystemVerilog and UVM Verification Course
Nadav Talmon

## Slide 2
You will:
Understand a DUT register specification
Implement a uvm_reg_adapter
Integrate a RAL model and predictor into the environment
Prepare the testbench for RAL-based sequences
You are not expected to complete full tests during class.

## Slide 3
Lab Structure
This lab is divided into four parts:
01
Understand the DUT and register specification
02
Inspect the generated RAL model
03
Implement the RAL adapter
04
Integrate RAL into the environment

## Slide 4
Part A: The Design Under Test (DUT)
The Goal
Understand what the hardware does before verifying it.
A1. Simple Timer Unit (STU)
The DUT is a Simple Timer Unit (STU) controlled entirely through registers.
Functional behavior
Loads a value from LOAD_VAL
Counts down once per clock cycle
Sets a DONE flag when the counter reaches zero
Control characteristics
Controlled through a CONTROL register
START is self-clearing
DONE is write-1-to-clear (W1C)
BUSY reflects internal activity and is read-only
These behaviors are intentional and will directly affect RAL behavior.

## Slide 5
Part B: Register Specification
The Goal
Understand the source of truth used to generate the RAL model.
B1. Register Specification File
Open:
Design/registers.csv
Identify:
Register names and offsets
Field access types (RW / RO / W1C)
Reset values
Which registers represent control vs status
This file is used to auto-generate the RAL model.

## Slide 6
Part C: Inspect the Generated RAL Model
The Goal
Understand what RAL gives you for free — and what it does not.
C1. Generated Code
Open:
Verification/ral/stu_ral.sv
Locate:
The stu_ral_model class (uvm_reg_block)
At least one uvm_reg
At least one uvm_reg_field
You are not expected to understand every line.
You are expected to understand:
How registers map to addresses
How fields map to bits
Where reset values are defined

## Slide 7
Part D: Implement the RAL Adapter
The Goal
Translate abstract RAL operations into real bus transactions.
This is the most critical part of the workshop.
D1. Adapter Responsibility
The adapter converts between:
uvm_reg_bus_op (generic RAL operation)
stu_seq_item (bus-specific transaction)
It determines:
Whether an operation is a READ or WRITE
Which address is accessed
Which data is transferred
How RAL learns what happened on the bus

## Slide 8
D2. File to Edit
Open:
Verification/ral/stu_reg_adapter.sv
You must implement:
reg2bus
bus2reg
Do not guess. Think carefully about who calls these functions and why.
D3. Concept Check (Before Coding)
You should be able to reason about:
Who calls reg2bus()?
Who calls bus2reg()?
Why does RAL care about write data?
Why does prediction exist at all?
If these are unclear — that is expected at this stage.

## Slide 9
Part E: Integrate RAL into the Environment
The Goal
Wire the RAL model into the UVM environment so it stays synchronized with hardware.
E1. File to Edit
Open:
Verification/env/stu_env.sv
You will:
Instantiate the RAL model
Instantiate the adapter
Instantiate the predictor
Connect predictor to the monitor
Bind the register map to the sequencer and adapter
E2. Integration Checklist
Before compiling, confirm:
The register model is built (build())
The adapter is assigned to the map
The predictor listens to the monitor
The predictor knows which adapter to use
Missing any one of these leads to silent errors.

## Slide 10
Part F: Compile and Reason
The Goal
Observe behavior and reason about architecture — not write tests yet.
Think Like a Verification Engineer
Ask yourself:
If hardware updates a status register internally, who updates the model?
If mirrored values are wrong, where would you debug?
What breaks if the adapter is incorrect but simulation still runs?
These questions matter more than finishing code.